## Slide 1
Intro to resilience modelling, simulation, and visualization in Python with fmdtools
Author: Daniel Hulse
Version 1.0

## Slide 2: Overview/Prerequisites
Overview of fmdtools
  Purpose
  Code structures
  Methods
  Syntax
Coding Activity
  Example model
  Workbook
    Model Instantiation
    Simulation
    Visualization/Analysis
You need a Python distribution!
(preferable Anaconda)
https://www.anaconda.com/products/individual
Download Slides:
/docs/Intro to Fmdtools
Right click “Save link as…”

## Slide 3: Why model system resilience?
We want to know how the system will respond to hazardous events, to:
  Reduce unforeseen maintenance/repairs
  Ensure system safety
  Check that system behavior will be robust to unforeseen events
In a hazardous scenario:
  Will the system fail to a safe condition?
  Will it recover?
  Or, will it wreak havoc on itself and the environment?

## Slide 4: What is resilience?
Fault Time
Nominal Performance
Faulty Performance
Recovery
No Recovery
Prevention
Recovery
Yodo, N., & Wang, P. (2016).
Resilience
Hazard
Nominal Scenario
Expected
Resilience:
Resilience over a set of hazardous scenarios

## Slide 5: Why use resilience in design?
Proactive
Design
Reactive
Design
Concept Design
Embodiment Design
Implementation
Establish resilience approach
Integrate resilient features in design
Verify resilient function
?
?
?
?
?
Retrofit for resilience
?
?
?
?
Design system
Choose concept
✔
✔
✔
✔
S1
S2
S3
Image 1 & 2 Credit: User’s Guide for the Commercial Modular Aero-Propulsion System Simulation (C-MAPSS)
Image 3 Credit: https://en.wikipedia.org/wiki/File:General_Electric_Passport.jpg
So we can make the system resilient-by-design

## Slide 6: Why fmdtools? Why not an existing tool?
Uncertainty Quantification tools: (e.g. OpenCossan)
  Doesn’t incorporate fault modelling/propagation/visualization aspects
MATLAB/modelica/etc. Fault Simulation tools
  Rely on pre-existing model/software stack
  Useful, but often difficult to hack/extend
Safety Assessment tools: (e.g. Alyrica, Hip-Hops)
  Focused on quantifying safety, not necessarily resilience
    (though they are related)
  Different model formalisms!

## Slide 7: Why fmdtools?
Expressive:
  Undirected graph propagation
    faults from any component can propagate to any other connected component
  General model representation—not a strict formalism
    Behavioral (equations), fault logic (if-else statements), etc.
  Dynamic simulation needed to quantify resilience
Research-oriented:
  Written in/relies on the Python stack
  Open source/free software
Enables design:
  Models can be parameterized an optimized!
  Provides tools to visualize and quantify simulation results

## Slide 8: Why not fmdtools?
Limitations:
  Doesn’t work with existing models in different software
    no integration with Simulink, modelica, etc. system models
  It’s research code
    Not yet fully tested outside of known use-cases
    Ongoing development may create problems for existing models

## Slide 9: What is fmdtools?
Analyze Resilience
Expected costs
Behavior over time
Plots/animations
Simulate Faults
Over each fault
Over each time
Record result histories
Construct Model
Function classes
Model class
Sample approach
Network Structure Model
Dynamic Behavioral Model
Hierarchical Model
Increasing Model Detail/Fidelity
Static Propagation Model
Stochastic Model
A Resilience-based Design Environment

## Slide 10: Repository
https://github.com/NASA-SW-VnV/fmdtools
/fmdtools - toolkit modules
/example_XXX – example models
  Example_pump - Simple model and tutorial/demonstration notebooks
  Example_multirotor - Example of several model types from "fmdtools: A Fault Propagation Toolkit for Resilience Assessment in Early Design.“
  Example_eps - Example of a static propagation model
  Example_tank - Example of a human error model implemented with components
/docs - additional documentation
/tests - automated software tests
Toolkit modules also available from PyPl (e.g. pip install fmdtools)

## Slide 11: Activity: Download and Install fmdtools
Make sure Python environment is installed
  e.g. https://www.anaconda.com/products/individual
Install fmdtools from PyPl:
  pip install fmdtools
Download workbook files from Github repository
  https://github.com/NASA-SW-VnV/fmdtools
  Navigate to /example_pump
  Right Click Tutorial_unfilled.ipynb and click “Save Link As” to download
  Right Click ex_pump.py and click “Save Link As” to download to your computer
Open the notebook and model!

## Slide 12: Structure: /fmdtools
Design
Simulation
Analysis
modeldef.py
Model class: representation of model functions, flows, behaviors, faults, etc.
  Function class
  Flow class, …
SampleApproach class: defines set of fault scenarios to represent the statistical expectation of resilience
NominalApproach class: defines set of nominal scenarios for simulating design/operational envelope
/faultsim
/resultdisp
networks.py
Quantification and visualization of metrics using a network model representation
propagate.py
Propagation of model behaviors in nominal and faulty scenarios
nominal(), one_fault()
singlefaults(), approach()
nominal_approach()
nested_approach()
graph.py
Visualization of simulation results on the model graph
plot.py
Plotting of system behaviors and costs over time
process.py
Processing of simulation results into metrics/statistics
tabulate.py
Display and export of simulation results as tables

## Slide 13: A typical work-flow
modeldef.py
Define model: System.py
Model Class:
Run parameters
Function/flow connections
Effects Classification
Function/Component Classes:
States
Behaviors
Simulate, visualize process model: Script.py or Notebook.ipynb
Model instantiation (e.g. mdl = Model())
Behavior simulation
  propagate.nominal(mdl), propagate.one_fault(mdl, fault) …
Results processing and visualization
  graph.show(mdl), plot.mdlhistvals(mdlhist) …
  tabulate.hist(mdlhist), tabulate.simplefmea(endclasses)…
/faultsim/propagate.py
/resultdisp/plot.py
/resultdisp /graph.py
…
Model, FxnBlock, Component
System
SampleApproach,
NominalApproach

## Slide 14: Defining a model
What do we want out of a model?
What functions/components and how much fidelity do we need?
  Network or behavioral?
  Dynamic or static?
  Functions or component architectures?
  Behaviors or failure logic?
What can go wrong? What are the faults/events?
What model parameters do we need to assess the resilience over?
What are the possible effects and how bad are they?

## Slide 15: Demonstration Model - Pump
/pump example/ex_pump.py
Functions: (nodes)
  Define behaviors, and faults of the of the system
  e.g. ImportSignal, ImportWater, MoveWater, ExportWater, ImportEE
Flows: (edges)
  Define the connections between functions of material, energy, signal, etc.
  e.g. Sig_1, Wat_1, EE_1, Wat_2

## Slide 16: Model structure
Function Classes
  Behaviors (I/O relationships)
  Faults (modes, probabilities)
  States (variable values)
  Failure logic (fault effects)
  Relationships to flows and components
Component Classes
  Similar to function classes, but no access to flows outside of function
Model Class
  Function/Flows
    Function/flow objects
    Graph of connections
  Run parameters
    Time, phases, units, etc
  Classification Method
    Method for determining fault effect costs
Flows
  State Dictionary
  EE = {voltage: 1.0, current:1.0}

## Slide 17: Defining a model – generic code
from fmdtools.modeldef import Model, FxnBlock
class System(Model):
def __init__(self, params={}, modelparams={}, valparams={})
super.__init__(params,modelparams,valparams)
self.add_flow(flowname, {value1:initvalue, value2: initvalue} …
self.add_fxn(functionname, [list of flows], fclass = DoSomething) …
self.build_model()
def end_condition(self, time):
(anything)
return True/False at end-state
def find_classification(self,resgraph, endfaults, endflows, scen, mdlhists):
(anything)
return {‘rate’:rate, ‘cost’:cost, ‘expected cost’=expected cost
(imports)
(defining model class for system)
(model initialization method)
(attach params to model)
(define model flows)
(add and connect functions)
(form model graph and run order, etc.)
(define how to classify model results)
design params
simulation params (e.g., start/end)
value params (fxns/flows to track)

## Slide 18: Defining functions – generic code
Class DoSomething(FxnBlock):
def __init__(self, name, flows):
super.__init__(name, flows,{state1: initval}, …)
self.failrate = failrate
self.assoc_modes({mode1:properties}, [opermodes])
self.assoc_randstate(statename, default)
def behavior(self, time):
if self.flowname.val1 > threshold: self.add_fault(‘mode1’)
if self.has_fault(‘mode1’): self.flowname.val2 = 0
else: self.flowname.val2 = 1
def dynamic_behavior(self,time):
self.state1.inc( = self.state1 + self.flowname.val2
def static_behavior(self,time):
Define class for DoSomething function
initialization method (can also be used to pass parameters)
add/associate model constructs:
flows, states, timers, components
Define fault/operational modes
generic method for all (static and dynamic) behavior
(different modes change behaviors)
method for dynamic (once per timestep) behaviors
(accumulation of a state over time)
Associate random states (for stochastic simulation)
method for static behaviors that can propagate between constructs during a single timestep

## Slide 19: Static Fault Propagation
Behaviors defined in .behavior(), .static_behavior(), and .condfaults()
Stored in mdl.staticfxns

## Slide 20: Dynamic Fault Propagation
Defined in .dynamic_behavior()
Runs once per timestep in a user-specified order.
Accessible in mdl.dynamicfxns
--------
Static/Dynamic propagation can be visualized using rd.graph.exec_order()

## Slide 21: Activity: Open and instantiate pump model
Review code:
  See pump code defining the Pump model class
  See pump code defining MoveWater function class
Open tutorial notebook
  Tutorial_unfilled.ipynb
Instantiate the model
  mdl = Pump()
Explore
  Try different parameters! Change things!
  What does the model directory look like? dir(mdl)

## Slide 22: Goal: Quantify Resilience With Simulation
Fault Time
Nominal Performance
Faulty Performance
Recovery
No Recovery
Prevention
Recovery
Yodo, N., & Wang, P. (2016).
Resilience
Hazard
Nominal Scenario
Expected
Resilience:
Resilience over a set of hazardous scenarios

## Slide 23: Simulation—things to consider
What are we trying to model:
The nominal performance of a system?
The performance of a system over a set of operational paremeters
The performance in a fault scenario?
The performance over a set of fault scenarios?
  What kind of set?

## Slide 24: Simulation types
Nominal performance
Performance over a set of possible operational parameters
Resilience over a set of fault modes
Resilience to a single fault or hazard
Resilience to a set of fault modes over a set of operational parameters

## Slide 25: Fault propagation aspects
Static/Dynamic propagation: How function states propagate to each other in a single time-step and multiple time-steps
  Undirected graph representation—states can effect all other connected states, and vice versa, in any order
Stochastic Propagation: Whether and how stochastic states are instantiated over time
  e.g. do we run with the “default” values of parameters, or do we sample from a random number generator?
Breadth of Scenarios: How hazards are represented as discrete scenarios to simulate
  What set of joint faults do we use? How many times are sampled?
  Operational scenarios and Joint operational/fault scenarios

## Slide 26: Behavioral Simulation Methods
propagate.nominal(mdl)
  Simulates system once with no fault—good for model setup
propagate.one_fault(mdl, function, fault, time=faulttime), .propagate.mult_fault(mdl, faultseq)
  Simulates system once with and without a fault
  Good for verifying/visualizing model behavior under a given fault
propagate.single_faults(mdl)
  Simulates the list of single fault modes
  Only use for static (single time-step) models & to gauge fault severity
propagate.approach(mdl, app)
  Simulates a set of fault modes over a set of times
  Useful for expected resilience quantification
  app defined in SampleApproach class
propagate.nominal_approach(mdl, nomapp), propagate.nested_approach(mdl,nomapp)
  Used for sampling the model over a range of parameters defined in a NominalApproach in nominal (nominal_approach) and faulty (nested_approach) scenarios.

## Slide 27: Simulation types
Nominal performance
propagate.nominal()
Performance over a set of possible operational parameters
propagate.
ominal_approach()
Resilience over a set of fault modes
propagate.approach()
Resilience to a single fault or hazard
propagate.one_fault()
propagate.mult_fault()
Resilience to a set of fault modes over a set of operational parameters
propagate.nested_approach()

## Slide 28: Definition of a fault sampling approach
app = SampleApproach(mdl,
faults = ‘all’/[list of faults]
phases = ‘all’/{fxn:phase:[s,e]}
modephases = {fxn:mode:{phases}}
jointfaults = {‘faults’:#,
‘jointfuncs’:True/False
‘pcond’: 0.##}
defaultsamp: = {‘samp’: ‘quad’/’fullint’/’evenspacing’…
‘numpts’: #
‘quad’: quadrature}
sampparams = {(fault, mode): sampparam}
(faults to include in the list)
(phases of each function to include (if model has phases))
(Number of joint-fault modes to simulate (e.g. None, 2,3,..))
(Whether function modes are mutually exclusive)
(Conditional probability for joint faults (ind. by default))
(how to represent phases)
(Number of samples to take in each phase)
(If a quadrature is used, the quadpy object)
(If a different approach is to be used for each fault, sampparam follows the defaultsamp structure)
(how function modes correlate to phases)

## Slide 29: Definition of a nominal sampling approach
nomapp = NominalApproach()
nomapp.add_seed_replicates(raingeid, seeds)
nomapp.add_param_replicates(paramfunc, rangeid, replicates)
nomapp.add_param_ranges(paramfunc, rangeid, *args, **kwargs
nomapp.add_rand_params(paramfunc, rangid, *fixedargs, **randvars)
Instantiate approach
Construct approach as a set of random seeds to instantiate in the model
Construct approach as the output of parameters in a function over x replicates
Construct approach as the output of a parameter function a range of arguments *args, and **kwargs
which may either be fixed or varied as a tuple defining the range (start, end, step)
Construct approach as the output of a parameter function a range fixed arguments *fixedargs
and stochastic variables generated in **kwargs as (randfunc, funcparam1, funcparam2)

## Slide 30: Activity: Propagate faults in the model
Run fault propagation methods:
  Nominal
  Fault(s)
  Approach
What do the results look like?
  endresults, resultshist, etc
Explore:
  What happens when you change SampleApproach parameters?
  What happens when you change model parameters?
  How do these methods compare in terms of computational time?

## Slide 31: Visualization, Quantification, Processing
Looking at a model
Looking at modelled quantities
Quantifying resilience
Saving/exporting results, etc

## Slide 32: /resultdisp
graph.py
Visualization of simulation results on the model graph
-set_pos(graph):
Manually positions of functions/flows in graph
-show(mdl/graph):
Show graph at end-state
-exec_order(mdl/graph)
Show dynamic/static order
-history(graphhist):
Shows set of graphs over history
-result(s)_from(mdl, reshist, t)
Shows model state at a particular time(s)
-animation_from(mdl, reshist,t)
Animates model states over given times
plot.py
Behavioral/Statistical Plotting
-mdlhist/s/vals(mdlhist):
Plots behavior of given states over time in a set of scenarios
-samplecost(app, endclasses):
Cost and rates of a set of faults
-costovertime(endclasses,app):
Cost of fault modes over time
-phases(mdlphases)
Function modes over time.
-nominal_vals_1d/2d/3d():
Simulation metric(s) in terms of input parameters
-nom/res_factor_comparison()
Comparison of simulation statistics over given factors
process.py
Processing of simulation results into metrics/statistics
-hists(mdlhists)/hist(mdlhist): processes result history for fmea/visualization
-heatmaps(reshist), etc: creates heatmap of respective quantities over time/runs
-totalcost(endclasses): calculates total expected cost
-end/overall_diff(endclasses):
Difference between nominal and faulty scenarios
-percent/average/rate/…
Various statistics for endclasses
tabulate.py
Display and export of simulation results as tables
-hist(mdlhist): Gives table of the history of model states.
-deghist(mdlhist, withstats): Gives table of all degraded functions and flows over time
-heatmaps(heatmap): Displays heatmap dictionary
-simple/phase/sum/fullfmea():
FMEA-like assessment with faults, probabilities, and costs.
-nominal/nested_stats():
Table of simulation statistics
-nom/res_factor_comparison()
Table of simulation statistics over given factors
Netgraph

## Slide 33: plot.py
Example Syntax:
rd.plot.mdlhistvals(mdlhist, ‘faultname’,
time=faulttime,
fxnflowvals={‘Flow1':[‘val1', ‘val2'],’flow2’:’val1’},
cols=2, timelabel="time (min)")
plot.py
Behavioral/Statistical Plotting
-mdlhist/s/vals(mdlhist):
Plots behavior of given states over time in a set of scenarios
-samplecost(app, endclasses):
Cost and rates of a set of faults
-costovertime(endclasses,app):
Cost of fault modes over time
-phases(mdlphases)
Function modes over time.
-nominal_vals_1d/2d/3d():
Simulation metric(s) in terms of input parameters
-nom/res_factor_comparison()
Comparison of simulation statistics over given factors

## Slide 34: graph.py
Example Syntaxes:
rd.graph.show(mdl.graph)
rd.graph.show(resgraph)
rd.graph.result_from(mdl, reshist, time,
gtype = ‘normal’/'bipartite’,
scale=2, pos=pos)
plot.py
Behavioral/Statistical Plotting
-mdlhist/s/vals(mdlhist):
Plots behavior of given states over time in a set of scenarios
-samplecost(app, endclasses):
Cost and rates of a set of faults
-costovertime(endclasses,app):
Cost of fault modes over time
-phases(mdlphases)
Function modes over time.
-nominal_vals_1d/2d/3d():
Simulation metric(s) in terms of input parameters
-nom/res_factor_comparison()
Comparison of simulation statistics over given factors

## Slide 35: tabulate.py
Example Syntaxes:
reshists, diffs, summaries = rd.process.hists(mdlhists)
fullfmea = rd.tabulate.fullfmea(endclasses, summaries)
phasefmea = rd.tabulate.phasefmea(endclasses, app)
tabulate.py
Display and export of simulation results as tables
-hist(mdlhist): Gives table of the history of model states.
-deghist(mdlhist, withstats): Gives table of all degraded functions and flows over time
-heatmaps(heatmap): Displays heatmap dictionary
-simple/phase/sum/fullfmea():
FMEA-like assessment with faults, probabilities, and costs.
-nominal/nested_stats():
Table of simulation statistics
-nom/res_factor_comparison()
Table of simulation statistics over given factors

## Slide 36: Activity: Visualize the results
Visualize the results
  Show model graph
  Show nominal performances
  Show performances in a nominal scenario
  Make a scenario-based fmea
Explore
  How can you show only the parameters you want? Or change the formatting?
  What does the behavior under other faults look like?
  What other analyses can you perform with these results?

## Slide 37: Further Reading
Explanatory Papers
D. Hulse, H. Walsh, A. Dong, C. Hoyle, I.Y. Tumer, C. Kulkarni, K. Goebel, “fmdtools: A Fault Propagation Toolkit for Resilience Assessment in Early Design“ IJPHM. Submitted
D. Hulse, C. Hoyle, I.Y. Tumer, K. Goebel, C. Kulkarni, “Temporal Fault Injection Considerations in Resilience Quantification.” ASME IDETC/CIE 2020, Design Automation Conference. IDETC2020-19287.
8. Stochastic Simulation
/example_pump/Stochastic Modelling.ipynb
1. Model Definition
/docs/Model Structure Visualization Tutorial.ipynb
3. Plotting/Visualization
/example_pump/Pump Example Notebook.ipynb
4. Fault Sampling Approaches
/docs/Nominal Approach Use-Cases.ipynb
6. Simulation Parallelism
/docs/Nominal Approach Use-Cases.ipynb
Modelling/Simulation Basics
2. Model Simulation
/example_multirotor/Demonstration.ipynb
Scenario Sampling
Advanced/Specialized Model Setup
7. Nominal/Nested Approaches
/docs/Nominal Approach Use-Cases.ipynb
9. Further Examples
/example_tank/Tank Analysis.ipynb
/example_eps/EPS Example Notebook.ipynb