## Slide 1
Fault Time
Nominal Performance
Faulty Performance
Recovery
No Recovery
Prevention
Recovery
Yodo, N., & Wang, P. (2016).
Resilience
Hazard
Nominal Scenario
Expected
Resilience:
Resilience over a set of hazardous scenarios

## Slide 2
Robustness Safety Threshold
Recovery Time Safety Threshold
Unsafe Disruptions
Resilience means taking a dynamic understanding of risk/safety
Safe Disruptions
Risk Outcomes
Considering resilience is important when our system has dynamic attributes, e.g.:
The system state changes over time
  (e.g., position, velocity, etc)
We can control this state
  (e.g., operators, autopilot)
Because we can use it to determine how to control the system to a safe outcome in unsafe circumstances and what design/operational features we need to enable this control

## Slide 3
Proactive
Design
Reactive
Design
Concept Design
Embodiment Design
Implementation
Establish resilience approach
Integrate resilient features in design
Verify resilient function
?
?
?
?
?
Retrofit for resilience
?
?
?
?
Design system
Choose concept
✔
✔
✔
✔
S1
S2
S3
Image 1 & 2 Credit: User’s Guide for the Commercial Modular Aero-Propulsion System Simulation (C-MAPSS)
Image 3 Credit: https://en.wikipedia.org/wiki/File:General_Electric_Passport.jpg
Idea: the system should be resilient-by-design

## Slide 4
Definition Packages
/define/block/function.py,
/define/container/state.py
/define/flow/base.py
/define/architecture/function.py
/define/container/mode.py, …
System Model File: model.py
State Classes
Flow Classes
Function Classes
Mode Classes
Model Classes
Parameter Classes
etc…
Analysis Script: Script.py or Notebook.ipynb
Model instantiation (e.g. mdl = Model())
Simulation
  result, history = propagate.one_fault(mdl, fault, t) …
Results processing and visualization
  ModelGraph(mdl).draw()
  History.plot_line(‘value’)
  etc…
Simulation Modules
/sim/propagate.py
/sim/sample.py
/sim/search.py
Analysis Modules
/analyze/phases.py
/analyze/tabulate.py
/analyze/phases.py …
FunctionArchitecture, Function, Flow, State…
Model
Class
ParameterSample, one_fault(), etc…
PhaseMap,
fmea(), etc…

## Slide 5
FunctionArchitecture: Agglomeration of Functions, Flows, and Hazard Metrics
Component: Sub-behavior internal to a Function with its own behaviors and properties, etc
Flow: Data Structures (inputs/outputs) that connect Functions
Function: Defines high-level system behaviors as well as failure modes and component architectures
State: Entries that define Function/Flow state

## Slide 6: Static Fault Propagation
Behaviors defined in .behavior(), .static_behavior(), and .condfaults()
Stored in mdl.staticfxns

## Slide 7: Dynamic Fault Propagation
Defined in .dynamic_behavior()
Runs once per timestep in a user-specified order.
Accessible in mdl.dynamicfxns
--------
Static/Dynamic propagation can be visualized using rd.graph.exec_order()

## Slide 8: Activity: Open and instantiate pump model
Review code:
  See pump code defining the Pump model class
  See pump code defining MoveWater function class
Open tutorial notebook
  Tutorial_unfilled.ipynb
Instantiate the model
  mdl = Pump()
Explore
  Try different parameters! Change things!
  What does the model directory look like? dir(mdl)

## Slide 9: Goal: Quantify Resilience With Simulation
Fault Time
Nominal Performance
Faulty Performance
Recovery
No Recovery
Prevention
Recovery
Yodo, N., & Wang, P. (2016).
Resilience
Hazard
Nominal Scenario
Expected
Resilience:
Resilience over a set of hazardous scenarios

## Slide 10
Nominal performance
propagate.nominal()
Performance over a set of possible operational parameters
propagate.
parameter_sample()
Resilience over a set of fault modes
propagate.
fault_sample()
Resilience to a single fault or hazard
propagate.one_fault()
propagate.sequence()
Resilience to a set of fault modes over a set of operational parameters
propagate.nested_sample()

## Slide 11
/graph
Graph-based visualizations.
result.py
Analysis and save/load of simulation results.
Result: Class for storing and analyzing results from a simulation specified in desired_result argument
tabulate.py
Construction of analyses based on samples.
FMEA: FMEA-like assessment with faults, probabilities, and costs.
Comparison: Class for comparing different metrics over different scenarios in a ParameterSample/Faultsample.
NominalEnvelope: Class for determining nominal envelope of system over a ParameterSample
common.py
Basic analysis utilities (plotting, calculations, etc) used throughout.
history.py
Logging, processing, and simulation histories.
History: Class for logging and analyzing results from a simulation specified by tracking options.
phases.py
Analysis of phases of operation in the system
PhaseMap: Class for interacting with model phases of operation for sampling and analysis.
from_hist(): method for generating PhaseMaps from throughout a model.
base.py
Generic graph-based visualizations.
Graph: Base class for displaying and interacting with graphs.
label.py
Defines graph labels.
model.py
Graph visualizations for models
ModelGraph: Class to represent model constructs as graphs
style.py
Defines node and edge styles.

## Slide 12
class StateName(State):
varname1: float = 1.0
varname2: str = “default_value”
class ParameterName(Parameter):
varname1: float = 1.0
varname1_range = (0.0, 10.0)
varname2 : str = “default_value”
varname2_set = (“default_value”, “other_possible_value”)
class ModeName(Mode):
fm_args = {‘fault_1’: (0.001, 200.0),
‘fault_2’: 0.00001, 100.0, {‘on’: 1.0}}
opermodes = [“off”, “on”]
mode: str = “off”
State classes are used to represent variables (called fields) that change over time
Parameter classes are used to represent variables that don’t change over time, with similar syntax to States
Mode classes are used to represent modes (faults and operational modes) that could occur in the system
Field name
Field type or class
Default initial value
varname1_range defines allowable range for the variable varname1
varname2_set defines allowable values for the field varname2
Dictionary of fault names and their optional properties (rate, repair cost, phases they could occur and their rates)
List of potential operational modes (if multiple)
Default mode (if multiple modes/not nominal)

## Slide 13
class FlowName(Flow):
__slots__ = ()
container_s = StateName()
container_p = ParameterName()
default_track = [‘s’,’m’]
def indicate_XXX(self, time):
Conditional statement (e.g., self.s.state>threshold) which is logged in the history and may be used to terminate simulations
Classes in fmdtools rely heavily on __slots__ for performance and type-safety. If no non-standard attributes are added, leave this blank.
Specifies which container classes play specific Flow roles (e.g., s corresponds to the state role, p corresponds to a parameter role, m corresponds to the mode role, etc)
These methods define Flow indicators and are called/tracked during simulation (in flow.i)
Specifies what should be tracked in the FxnBlock history (fxnname.h) by default. May be a dict ({role:value}), list ([role1, role2]), or string (“all”,”none”, etc). Overwritten by the track parameter during model instantiation.

## Slide 14
class FunctionName(Function):
__slots__ =(‘flowname1’,)
container_s = FunctionState
container_m = FunctionMode
container_t = FunctionTime
flow_flowname1 = FlowClass1
flownames = {“outsideflowname”:”flowname1”}
default_sp = {‘end_time’: 100}
default_track = [‘s’,’m’]
def init_block(self, **kwargs):
<e.g., self.s.x = 2.0>
def static_behavior(self, time):
Runs only in static propagation steps
def dynamic_behavior(self, time):
Runs only in dynamic propagation steps
def behavior(self, time):
Runs in static propagation step (same as static_behavior)
def condfaults(self, time):
Runs in both static and dynamic propagation steps prior to behaviors and internal fault propagation (to components and actions)
def indicate_XXX(self, time):
Conditional statement (e.g., self.s.state>threshold) which is logged in the history and may be used to terminate simulations
def find_classification(self, time):
Returns a Result dictionary (calculated at completion)
Specifies what should be tracked in the FxnBlock history (fxnname.h) by default. May be a dict ({role:value}), list ([role1, role2]), or string (“all”,”none”, etc). Overwritten by the track parameter during model instantiation.
flow_XXX is used to append a flow of given type that is named XXX to the function class. If the flow(s) has a different name outside the function (optional), flownames matches the external name to the internal name
Specifies which classes play specific FxnBlock roles (e.g., s corresponds to the state role, m corresponds to the mode role, etc)
Optional method to call to set up FxnBlock in ways not already defined by role initalization (e.g., attaching local MultiFlows or setting initial values for States from Parameter)
These methods define the behavior of the FxnBlock and thus simulate at each time-step of the simulation.
These methods define FxnBlock indicators and are called/tracked during simulation (in fxnname.i)
Default keyword arguments for SimParam. Only necessary when the functionblock will be simulated individually.
This method defines the Result to be returned when simulated individually
Tuple of flows must be specified in __slots__

## Slide 15
class ArchitectureName(FunctionArchitecture):
__slots__ = ()
container_p= ModelParam
default_sp = {‘end_time’: 100}
default_track = [“fxns”, “flows]
def init_architecture(self, **kwargs):
self.add_flow(“flowname”, FlowClass)
…
self.add_fxn(“functionname”, FunctionClass, “flowname1”, “flowname2”)
…
def indicate_XXX(self, time):
Conditional statement
(e.g., self.fxns[“functionname”].s.state>threshold)
which is logged in the history and may be used to terminate simulations
def find_classification(self, time):
Returns a Result dictionary (calculated at completion)
Specifies what should be tracked in the Model history by default. May be a dict ({role:value}), list ([role1, role2]), or string (“all”,”none”, etc). Overwritten by the track option in propagate.
Points to a Parameter representing immutable model characteristics instantiated at the start of the simulation
Method to instantiate the model and define its structure:,
.add_flow is used to instantiate a flow
.add_fxn is used to instantiate a function and attach connected flows
These methods define Model indicators and are called/tracked during simulation (in modelname.i)
Default keyword arguments for SimParam. Defines max time of the simulation, along with phases, timestep, units, etc.
This method defines the Result to be returned by the model.
Architecture classes are usually given empty __slots__

## Slide 16
Flexible
Powerful
Efficient