## Slide 1
Intro to resilience modelling, simulation, and visualization in Python with fmdtools
Author: Daniel Hulse

## Slide 2: Overview/Prerequisites
Overview of fmdtools
  Purpose
  Code structures
  Methods
  Syntax
Coding Activity
  Example model
  Workbook
    Model Instantiation
    Simulation
    Visualization/Analysis
You need a Python distribution!
(preferable Anaconda)
https://www.anaconda.com/products/individual
Download Slides:
github.com/DesignEngrLab/fmdtools/tree/main/docs
Right click “Save link as…”

## Slide 3: Why model system resilience?
We want to know how the system will respond to hazardous events, to:
  Reduce unforeseen maintenance/repairs
  Ensure system safety
  Check that system behavior will be robust to unforeseen events
In a hazardous scenario:
  Will the system fail to a safe condition?
  Will it recover?
  Or, will it wreak havoc on itself and the environment?

## Slide 4: What is resilience?
Fault Time
Nominal Performance
Faulty Performance
Recovery
No Recovery
Prevention
Recovery
Yodo, N., & Wang, P. (2016).
Resilience
Hazard
Nominal Scenario
Expected
Resilience:
Resilience over a set of hazardous scenarios

## Slide 5: Why use resilience in design?
Proactive
Design
Reactive
Design
Concept Design
Embodiment Design
Implementation
Establish resilience approach
Integrate resilient features in design
Verify resilient function
?
?
?
?
?
Retrofit for resilience
?
?
?
?
Design system
Choose concept
✔
✔
✔
✔
S1
S2
S3
Image 1 & 2 Credit: User’s Guide for the Commercial Modular Aero-Propulsion System Simulation (C-MAPSS)
Image 3 Credit: https://en.wikipedia.org/wiki/File:General_Electric_Passport.jpg
So we can make the system resilient-by-design

## Slide 6: Why fmdtools? Why not an existing tool?
Uncertainty Quantification tools: (e.g. OpenCossan)
  Doesn’t incorporate fault modelling/propagation/visualization aspects
MATLAB/modelica/etc. Fault Simulation tools
  Rely on pre-existing model/software stack
  Useful, but often difficult to hack/extend
Safety Assessment tools: (e.g. Alyrica, Hip-Hops)
  Focused on quantifying safety, not necessarily resilience
    (though they are related)
  Different model formalisms!

## Slide 7: Why fmdtools?
Expressive:
  Undirected graph propagation
    faults from any component can propagate to any other connected component
  General model representation—not a strict formalism
    Behavioral (equations), fault logic (if-else statements), etc.
  Dynamic simulation needed to quantify resilience
Research-oriented:
  Written in/relies on the Python stack
  Open source/free software
Enables design:
  Models can be parameterized an optimized!
  Provides tools to visualize and quantify simulation results

## Slide 8: Why not fmdtools?
Limitations:
  Deterministic modelling paradigm
    no ability to model non-deterministic behaviors
  Doesn’t work with existing models in different software
    no integration with Simulink, modelica, etc. system models
  Not targeted for safety/fault tree calculation
  It’s research code!

## Slide 9: What is fmdtools?
A modelling framework
Simulation methods
Visualizations/Metrics
…
A design environment

## Slide 11: GitHub Repository
github.com/DesignEngrLab/fmdtools
/fmdtools – toolkit modules
/XX example – example models
Documentation in /docs, readme, examples
Toolkit modules also available from PyPl
(e.g. pip install fmdtools)

## Slide 12: Activity: Download and Install fmdtools
Make sure Python environment is installed
  e.g. https://www.anaconda.com/products/individual
Install fmdtools from PyPl:
  pip install fmdtools
Download workbook files from Github repository
  https://github.com/DesignEngrLab/fmdtools
  Navigate to /pump example
  Right Click Tutorial_unfilled.ipynb and click “Save Link As” to download
  Right Click ex_pump.py and click “Save Link As” to download to your computer
Open the notebook and model!

## Slide 13: Structure: /fmdtools
Design
Simulation
Analysis
modeldef.py
Model class: representation of model functions, flows, behaviors, faults, etc.
  Function class
  Flow class
  Component class
  …
SampleApproach class: defines set of fault scenarios to represent the statistical expectation of resilience
/faultsim
/resultdisp
networks.py
Quantification and visualization of metrics using a network model represtenation
propagate.py
Propagation of model behaviors in nominal and faulty scenarios
nominal()
one_fault()
singlefaults()
approach()
graph.py
Visualization of simulation results on the model graph
plot.py
Plotting of system behaviors and costs over time
process.py
Processing of simulation results into metrics/statistics
tabulate.py
Display and export of simulation results as tables

## Slide 14: A typical work-flow
modeldef.py
Define model: System.py
Model Class:
Run parameters
Function/flow connections
Effects Classification
Function/Component Classes:
States
Behaviors
Simulate, visualize process model: Script.py or Notebook.ipynb
Model instantiation (e.g. mdl = Model())
Behavior simulation
  propagate.nominal(mdl), propagate.one_fault(mdl, fault) …
Results processing and visualization
  graph.show(mdl), plot.mdlhistvals(mdlhist) …
  tabulate.hist(mdlhist), tabulate.simplefmea(endclasses)…
/faultsim/propagate.py
/resultdisp/plot.py
/resultdisp /graph.py
…
Model, FxnBlock, Component
System
SampleApproach

## Slide 15: Defining a model
What do we want out of a model?
What functions/components and how much fidelity do we need?
  Network or behavioral?
  Dynamic or static?
  Functions or component architectures?
  Behaviors or failure logic?
What can go wrong? What are the faults/events?
What are the possible effects and how bad are they?

## Slide 16: Demonstration Model - Pump
/pump example/ex_pump.py
Functions: (nodes)
  Define behaviors, and faults of the of the system
  e.g. ImportSignal, ImportWater, MoveWater, ExportWater, ImportEE
Flows: (edges)
  Define the connections between functions of material, energy, signal, etc.
  e.g. Sig_1, Wat_1, EE_1, Wat_2

## Slide 17: Model structure
Function Classes
  Behaviors (I/O relationships)
  Faults (modes, probabilities)
  States (variable values)
  Failure logic (fault effects)
  Relationships to flows and components
Component Classes
  Similar to function classes, but no access to flows outside of function
Model Class
  Function/Flows
    Function/flow objects
    Graph of connections
  Run parameters
    Time, phases, units, etc
  Classification Method
    Method for determining fault effect costs
Flows
  State Dictionary
  EE = {voltage: 1.0, current:1.0}

## Slide 18: Defining a model – generic code
from fmdtools.modeldef import Model, FxnBlock
class System(Model):
def __init__(self, params={})
super.__init__(params=params, modelparams = {phases, times, timestep})
self.add_flow(flowname, {value1:initvalue, value2: initvalue} …
self.add_fxn(functionname, [list of flows], fclass = DoSomething) …
self.construct_graph()
def find_classification(self,resgraph, endfaults, endflows, scen, mdlhists):
(anything)
return {‘rate’:rate, ‘cost’:cost, ‘expected cost’=expected cost
(imports)
(defining model class for system)
(model initialization method)
(define run parameters)
(define model flows)
(add and connect functions)
(form model graph)
(define how to classify model results)

## Slide 19: Defining functions – generic code
Class DoSomething(FxnBlock):
def __init__(self, flows):
super.__init__([flownames],flows,{state1: initval}, …)
self.failrate = failrate
self.assoc_modes({mode1:[proportion,[phases],repcost]})
def condfaults(self, time):
if self.flowname.val1 > threshold: self.add_fault(‘mode1’)
def behavior(self, time)
if self.has_fault(‘mode1’): self.flowname.val2 = 0
else: self.flowname.val2 = 1
if time>self.time:
self.state1 = self.state1 + self.flowname.val2
(Define class for DoSomething function)
(initialization method (can also be used to pass parameters))
(add/associate model constructs:
flows, states, timers, components)
(Define faults and probability model)
(optional method for failure logic)
(function enters fault mode under given condition)
(method for system behavior)
(different modes change behaviors)
(dynamic behaviors are placed in an if time>self.time statement)
(accumulation of a state over time)

## Slide 20: Activity: Open and instantiate pump model
Review code:
  See pump code defining the Pump model class
  See pump code defining MoveWater function class
Open tutorial notebook
  Tutorial_unfilled.ipynb
Instantiate the model
  mdl = Pump()
Explore
  Try different parameters! Change things!
  What does the model directory look like? dir(mdl)

## Slide 21: Fault Simulation and Propagation
What are we trying to model:
The nominal performance of a system?
The performance in a fault scenario?
The performance over a set of fault scenarios?
  What kind of set?

## Slide 22: What if we want to quantify resilience
Fault Time
Nominal Performance
Faulty Performance
Recovery
No Recovery
Prevention
Recovery
Yodo, N., & Wang, P. (2016).
Resilience
Hazard
Nominal Scenario
Expected
Resilience
Simulate Nominal Performance
Simulate Fault Scenario Performance
Simulate Performance Over Set of Fault Scenarios

## Slide 23: Fault propagation – how it works
Static propagation: How function states propagate to each other in a single time-step
  Undirected graph representation—states can effect all other connected states, and vice versa, in any order
Dynamic propagation: How model states unfold over time

## Slide 24: Static Fault Propagation

## Slide 25: Dynamic Fault Propagation

## Slide 26: Behavioral Propagation Methods
propagate.nominal(mdl)
  Simulates system with no fault—good for model setup
propagate.one_fault(mdl, function, fault, time=faulttime)
  Simulates system with and without a fault
  Good for verifying/visualizing model behavior under a given fault
propagate.single_faults(mdl)
  Simulates the list of single fault modes
  Only use for static (single time-step) models & to gauge fault severity
propagate.approach(mdl, app)
  Simulates a set of fault modes over a set of times
  Useful for expected resilience quantification
  app defined in SampleApproach class

## Slide 27: Propagation of a fault approach
Goal: Quantify expected resilience over a set of fault modes and operational phases
  What times—all? 1-2? Several?
  What modes—all modes? A selection of modes? Joint fault modes?

## Slide 28: Propagation of a fault approach
app = SampleApproach(mdl,
faults = ‘all’/[list of faults]
phases = ‘all’/{fxn:phase:[s,e]}
modephases = {fxn:mode:{phases}}
jointfaults = {‘faults’:#,
‘jointfuncs’:True/False
‘pcond’: 0.##}
defaultsamp: = {‘samp’: ‘quad’/’fullint’/’evenspacing’…
‘numpts’: #
‘quad’: quadrature}
sampparams = {(fault, mode): sampparam}
(faults to include in the list)
(phases of each function to include (if model has phases))
(Number of joint-fault modes to simulate (e.g. None, 2,3,..))
(Whether function modes are mutually exclusive)
(Conditional probability for joint faults (ind. by default))
(how to represent phases)
(Number of samples to take in each phase)
(If a quadrature is used, the quadpy object)
(If a different approach is to be used for each fault, sampparam follows the defaultsamp structure)
(how function modes correlate to phases)

## Slide 29: Activity: Propagate faults in the model
Run fault propagation methods:
  Nominal
  Fault(s)
  Approach
What do the results look like?
  endresults, resultshist, etc
Explore:
  What happens when you change SampleApproach parameters?
  What happens when you change model parameters?
  How do these methods compare in terms of computational time?

## Slide 30: Visualization, Quantification, Processing
Looking at a model
Looking at modelled quantities
Quantifying resilience
Saving/exporting results, etc

## Slide 31: /resultdisp
graph.py
Visualization of simulation results on the model graph
-set_pos(graph):
Manually positions of functions/flows in graph
-show(mdl/graph):
Show graph at end-state
-history(graphhist):
Shows set of graphs over given history
-result(s)_from(mdl, reshist, t)
Shows model state at a particular time(s)
-animation_from(mdl, reshist,t)
Animates model states over given times
plot.py
Plotting of system behaviors and costs over time
-mdlhist/mdlhistvals(mdlhist):
Plots behavior of given states over time in a given faulty and nominal scenario
-samplecost(app, endclasses):
Plots costs and rates of a set of faults injected over time in an approach
-costovertime(endclasses,app):
Plots the total expected cost of faults over time
process.py
Processing of simulation results into metrics/statistics
-hists(mdlhists)/hist(mdlhist): processes result history for fmea/visualization
-heatmaps(reshist), etc: creates heatmap of respective quantities over time/runs
-totalcost(endclasses): calculates total expected cost
tabulate.py
Display and export of simulation results as tables
-hist(mdlhist): Gives table of the history of model states.
-deghist(mdlhist, withstats): Gives table of all degraded functions and flows over time
-heatmaps(heatmap): Displays heatmap dictionary in tabular form
-simple/phase/sum/fullfmea():
Gives FMEA-like assessment of the effects of faults/scenarios and their probability and costs
Netgraph

## Slide 32: plot.py
plot.py
Plotting of system behaviors and costs over time
-mdlhist/mdlhistvals(mdlhist):
Plots behavior of given states over time in a given faulty and nominal scenario
-samplecost(app, endclasses):
Plots costs and rates of a set of faults injected over time in an approach
-costovertime(endclasses,app):
Plots the total expected cost of faults over time
Example Syntax:
rd.plot.mdlhistvals(mdlhist, ‘faultname’,
time=faulttime,
fxnflowvals={‘Flow1':[‘val1', ‘val2'],’flow2’:’val1’},
cols=2, timelabel="time (min)")

## Slide 33: graph.py
graph.py
Visualization of simulation results on the model graph
-set_pos(graph):
Manually positions of functions/flows in graph
-show(mdl/graph):
Show graph at end-state
-history(graphhist):
Shows set of graphs over given history
-result(s)_from(mdl, reshist, t)
Shows model state at a particular time(s)
-animation_from(mdl, reshist,t)
Animates model states over given times
Example Syntaxes:
rd.graph.show(mdl.graph)
rd.graph.show(resgraph)
rd.graph.result_from(mdl, reshist, time,
gtype = ‘normal’/'bipartite’,
scale=2, pos=pos)

## Slide 34: tabulate.py
tabulate.py
Display and export of simulation results as tables
-hist(mdlhist): Gives table of the history of model states.
-deghist(mdlhist, withstats): Gives table of all degraded functions and flows over time
-heatmaps(heatmap): Displays heatmap dictionary in tabular form
-simple/phase/sum/fullfmea():
Gives FMEA-like assessment of the effects of faults/scenarios and their probability and costs
Example Syntaxes:
reshists, diffs, summaries = rd.process.hists(mdlhists)
fullfmea = rd.tabulate.fullfmea(endclasses, summaries)
phasefmea = rd.tabulate.phasefmea(endclasses, app)

## Slide 35: Activity: Visualize the results
Visualize the results
  Show model graph
  Show nominal performances
  Show performances in a nominal scenario
  Make a scenario-based fmea
Explore
  How can you show only the parameters you want? Or change the formatting?
  What does the behavior under other faults look like?
  What other analyses can you perform with these results?

## Slide 36: Further Reading and Links
Repository
https://github.com/DesignEngrLab/fmdtools
https://doi.org/10.5281/zenodo.3828048
Explanatory Paper
D. Hulse, H. Walsh, A. Dong, C. Hoyle, I.Y. Tumer, C. Kulkarni, K. Goebel, “fmdtools: A Fault Propagation Toolkit for Resilience Assessment in Early Design“ IJPHM. Submitted
Details on Fault Sampling
D. Hulse, C. Hoyle, I.Y. Tumer, K. Goebel, C. Kulkarni, “Temporal Fault Injection Considerations in Resilience Quantification.” ASME IDETC/CIE 2020, Design Automation Conference. IDETC2020-19287.